## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Low Latency Deterministic Networks (LLDN) in IEEE 802.15.4]
Date Submitted: [11 March, 2015]
Source: [Michael Bahr, Ludwig Winkel] Company [Siemens AG]
Address [Otto-Hahn-Ring 6, 81739 München, Germany]
Voice:[+49-89-636-49926], FAX: [Add FAX number], E-Mail:[bahr et siemens dod com]
Re: [Motivation for Low Latency Deterministic Networks (LLDN) in IEEE 802.15.4 in response to LLDN-related problems in IEEE 802.15.4 REVc]
Abstract: [Motivation for Low Latency Deterministic Networks (LLDN) in IEEE 802.15.4 and outlook on fixing the issues with the LLDN mode in IEEE 802.15.4 REVc]
Purpose: [Motivation for Low Latency Deterministic Networks (LLDN) in IEEE 802.15.4 in order to keep the LLDN specification of IEEE 802.15.4e (with fixed issues) in the REVc of IEEE 802.15.4.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Low Latency Deterministic Networks in IEEE 802.15.4
IEEE 802.15.4e defines Low Latency Deterministic Networks (LLDN mode)
Target at industrial applications with low latency requirements (≤ 2 ms per device) such as factory automation
  Basic concept: Low latency through short data packets in short dedicated timeslots of fixed length
  Mechanisms for flexible usage and configuration of time slots (shared group timeslots)

## Slide 3: Use Cases for IEEE 802.15.4e Low Latency Deterministic Networks (LLDN)
factory automation
automotive production lines
  robots
  suspension tracks
  portable
machine tools
  milling, turning
  robot revolver
filling
cargo
  airport logistics
  post
packaging industry
special engineering
conveyor technique

## Slide 4: Network Topology
star topology
LLDN PAN coordinator
devices
  sensors: unidirectional data exchange from devices to gateway
  actuators: bidirectional data exchange between devices and gateway
  management devices (temporary)

## Slide 5: Requirements and Assumptions for Low Latency Deterministic Networks (LLDN)
Requirements
usage in factory automation possible
high determinism, high reliability
low latency:
  transmission of sensor data in  10 ms ( 2 ms per device)
  low round-trip time
  short duration between subsequent transmissions
  small data: might be only 1 octet
high performance cyclic communication
relatively short communication distance
many devices per gateway
  might be more than 100 sensors per LLDN PAN coordinator
   trade-off with latency!
  common size of LLDN network only a few devices
Assumptions
controlled environment (factory floor)
off-line configuration for optimal performance
network planning
network management and frequency planning for avoidance of co-existence issues

## Slide 6: Why LLDN in IEEE 802.15.4?
good coexistence with IEEE 802.11 Wireless LAN
  3 non-overlapping channels for IEEE 802.11
  4 channels for IEEE 802.15.4
sufficient range
worldwide acceptance
worldwide standard
common wireless technology in industrial applications
North America
(similar worldwide)

## Slide 7: LLDN in IEEE 802.15.4 REVc
Low Latency Deterministic Networks (LLDN) part of IEEE 802.15.4e
During the revision process of IEEE 802.15.4 (REVc), problems and issues with LLDN have been discovered (see document 15-14/224)
Experts are now available for solving the LLDN issues
  First responses to LLDN-related issues are provided in document 15-15/174
  Base text for LLDN for re-insertion into IEEEW 802.15.4 REVc document provided in document 15-15/245 (text based on IEEE 802.15.4 REVc DF3)
For any arising issues related to LLDN and the revision process, please contact the authors
Necessary efforts for keeping LLDN in IEEE 802.15.4 will be undertaken

## Slide 8: Summary
Keep Low Latency Deterministic Networks (LLDN) in IEEE 802.15.4
Keep IEEE 802.15.4 ready with LLDN for the next step of wireless communication in industrial applications: low latency wireless
  Factory automation and similar use cases
  Important for Internet of Things (IoT) and future smart manufacturing
  Several calls for funded projects in the area of low latency wireless underway in Europe